## Slide 1: Previous Lecture
Whenever there is a potential difference between two points in a conductor…
… there is an electric field at those points
Whenever there is an electric field in a conductor, there are moving charges
Youtube: Lecture 16: https://youtu.be/PzULPcejP4I
Lecture 17: https://youtu.be/f5Kx9Kja1ao

## Slide 2: Current
OpenStax Chapter 20.1
Connecting wire across a potential difference results in current
Current flows from high potential to low potential
  It is conserved in a wire
  Also conserved at junctions

## Slide 3: Moving Charges
We’ve focused on stationary charges and well defined motion of small groups of charges
When larger groups of charges are moving, we’ll focus on “current”
Current (I) is motion of charges
SI unit: ampere (A); 1 A = 1 C / s
(often called “amp”)
http://en.wikipedia.org/wiki/File:Ampere_Andre_1825.jpg
Current through surface
Time for that charge to pass by
Charge that passes through

## Slide 4: How to start Current?
Inside Materials, Two Necessary Ingredients
Potential Difference
Means electric field and which leads to electric force
For isolated charges this is enough to get them moving
Path for charges to follow
Charges don’t spontaneously leave material so will flow through conductors
Can connect plates of capacitor, terminals of battery, etc.

## Slide 5: What Moves in a Metal?
Are the moving charges protons, electrons, or both?
Experiments show that only electrons move
(this matches idea of conductor as “sea of electrons”)
BUT: current is considered to be flow of “positive charge carriers”
+++++++
–––––––
e–
i.e. currents will be drawn going from high potential to low
(it is the convention used in current flow)
This is opposite the actual motion of electrons
I

## Slide 6: What Does Current Do?
If a wire is left connected long enough charged objects will discharge (battery will die, etc.)
While charges are flowing through a wire:
Wire Heats Up
Devices (like light bulbs) function
These two are closely related
Compass (that shows direction) readings change
(we’ll discuss this last one later in the course)

## Slide 7: Places Currents Show Up
Nature:
Lightning
10,000 A
0.00001 A
Nerve Impulse
Technology:
Hearing Aid
0.0001 A
Light bulbs
0.5 – 1 A
Toasters
10 A
Currents & You:
Detect
Hurt
Lethal
0.001 A
0.01 A
Severe Burns
Landline Phone
0.03 A
0.5 A
Burns
0.1 A
10 A
If DC & across heart (<0.1 A if AC)
Anything with a plug or battery
Phone Charger
0.1 A

## Slide 8: Motion of Charges
Electrons in any material at room temperature move around randomly, usually around fixed locations
Electrons have “drift velocity” opposite the direction of the electric field
If an electric field is applied, electrons try to move in a particular direction determined by the field
Electrons can interact with atoms and/or ions in the material
(i.e. collide and bounce off)
© 2010 Pearson Education, Inc.

## Slide 9: Conservation of Current
Direction of E-Field
For an electron to pass through the left ring but not the right, what would have to happen?
e–
Violate concepts like Newton’s 2nd Law, Conservation of Mass, or Conservation of Charge
Conservation of Current: Any current going into a part of a wire comes out the other side
(& Current)

## Slide 10: Kirchhoff’s Junction Law
Specific application of Conservation of Current
Analysis of what happens when two or more wires join together:
Current going into junction equals current going out
I1
I2
I3
If I1 = 2 A and I2 = 0.8 A,
then I3 = 1.2 A
http://en.wikipedia.org/wiki/File:Gustav_Robert_Kirchhoff.jpg

## Slide 11: Using Junction Law
I1 = 5 A
I2 = 2 A
I3 = ?
I5 = 3 A
I4 = 1 A
2 A up
2 A down
5 A down
9 A up
9 A down
I flowing in = I flowing out
I1 + I2 + I5 = I3 + I4
I3 = (5 + 2 + 3) – 1 A
I3 = 9 A
Junction

## Slide 12: Using the Junction Law
Ia = 6 A
What is current Iw?
Iw
Choose a direction for Iw
(if calculated current is negative, then Iw is opposite to direction chosen)
Ix
Iy
Iz
Iw =
Iw = Ib + Ic
Ib = 3 A
Ic = 2 A
Id = 1 A
= 5 A
What is current Ix?
A. 7 A, right B. 3 A, right C. 5 A, right D. 2 A, right E. 4 A, left
5 A, down
SIinto junction = SIout of junction

## Slide 13: Resistance
OpenStax Chapter 20.2
Resistance measures how hard it is for current to flow
  Depends on material and shape
  Increases with length, decreases with area

## Slide 14: Conservation of Current and “Circuit Elements”
Circuit Element: any part of a circuit that isn’t just a wire
Do they “use” current up?
Short answer: no
(otherwise negative charge would build up until current stopped)
Current occurs because electrons are trying to get from one side of battery to the other
© 2010 Pearson Education, Inc.
But: electrons interact with matter as current flows (slide 8)

## Slide 15: Changing Current
Two options to set up different currents :
Change potential difference (V):
increase V to increase current
Change what the current passes through:
Current will be much higher through metal than wood
Material
Length
Lower current in Longer path (more stuff in the way)
Area
Bigger current for Broader path (more avenues to pass through)

## Slide 16: Resistance
Measure of an object’s ability to “resist” current,
(i.e. like friction to flow of charges)
(higher for poor conductors)
Resistance of Object
Cross Section Area of Object
Length of Object
Resistivity of Material
SI Units of Resistance: ohm (W); 1 W = 1 V / A
Pretty much any object is a “resistor”
all objects of Same Material have the Same Resistivity [SI Units of Resistivity: ohm meter (W.m)]
1 m of 22 gauge Copper Wire:
0.05 W
1 m of 22 gauge Wood Dowel:
109 W

## Slide 17: Analyzing Resistor
A 1.20 m long cylinder has a resistance of 0.064 W. If it is made of nichrome (r = 1.5 × 10–6 W.m), what is its radius?
2.8 × 10–2 mm
1.0 mm
3.0 mm
4.0 mm
1.3 × 105 mm
First find cross sectional area
= 2.8 × 10–5 m2
Then find radius:
= 3.0 × 10–3 m

## Slide 18: Conceptual Analysis of Resistor
Two cylinders are made of copper. The first has a length L1, resistance R1, and mass m1. The second also has mass m1 but has a length of 2 L1. What is the second cylinder’s resistance?
R1 / 4
R1 / 2
R1
2 R1
4 R1
Same material so they have the same resistivities and densities
Same density and mass means same volume
Volume = A1 L1 = A2 L2
A1 L = A2 (2 L)
A2 = A1 / 2

## Slide 19: Ohm’s Law
OpenStax Chapter 20.2
Resistance relates potential difference to current
  Ohm’s Law: I = DV / R
  Resistors obey Ohm’s Law for just about all voltages

## Slide 20: Potential, Resistance, and Current Ohm’s Law
Ohm’s Law: relates resistance, potential and current:
Current passing through object
Resistance of object
Potential Difference across object
Resistance is often measured by graphing current vs. potential and looking for the slope
http://en.wikipedia.org/wiki/File:Ohm3.gif
Ohm

## Slide 21: Problem with Ohm’s Law
When two batteries are connected end to end, and a copper wire (with R = 0.15 W) is connected across them, the current through the wire is 20 A). What is the potential difference of one of the batteries?
+
–
+
–
3 V
1.5 V
133 V
6 V
266 V
(Find and divide by 2)

## Slide 22: Problem with Ohm’s Law [1]
When two batteries are connected end to end, and a 10 cm long copper wire is connected across them, the current through the wire is 3 A. What would be the current through a 30 cm long copper wire (with the same gauge as the first) connected across just one of the batteries?
1.0 V
0.5 A
4.5 A
9 A
1.5 A
+
–
+
–
+
–
First wire:
Second wire:

## Slide 23: Problem with Ohm’s Law [2]
1.0 V
0.5 A
4.5 A
9 A
1.5 A
Suppose: potential difference of one battery = e and, resistance of first wire = R1
First wire
Second wire
Resistance
Potential Difference
Current
DV1 = 2e
DV2 = e = DV1 /2
When two batteries are connected end to end, and a 10 cm long copper wire is connected across them, the current through the wire is 3 A. What would be the current through a 30 cm long copper wire (with the same gauge as the first) connected across just one of the batteries?

## Slide 24: Problem with Resistance and Potential
Two 1.5 V batteries are connected end to end with a wire made of copper (r = 1.7 × 10–8 Wm) connected from the positive terminal of one to the negative terminal of the other. If the wire is 11 cm long and has a diameter of 0.08 mm (approximately 40 gauge wire; A = 5.0 × 10–9 m2) what will the current through the wire be?
+
–
+
–
Note: Batteries are potential sources, not current sources
(current depends on both battery potential and resistance in circuit)
6.2 nA
1.2 nA
0.15 mA
4.0 A
8.1 A

## Slide 25: Wires
Metal Wires can be treated like resistors with very low resistance
An ideal wire is one that has zero resistance
(so, potential difference across an ideal wire is also zero regardless of current, because V = I R)
Real wires have resistances so low we’ll assume that they’re 0 W
Superconductors actually do have zero resistance
Current once started will never stop in a superconductor

## Slide 26: Battery vs. Wire Potential Differences
A battery has a potential difference of DVbatt (often called e)
How is potential measured?
If a wire is connected to the terminals, what is its potential difference DVwire?
+
–
by comparing two probes of voltmeter
Voltmeter can’t tell what it measures potential of: DVwire = DVbatt
A second wire would also have DVwire = DVbatt

## Slide 27: Circuits
OpenStax Chapter 20.2, 21.1

## Slide 28: Electric Circuits
Network of electric components
Electric components affect:
- potential difference (a.k.a. voltage)
(
- current (I)
- resistance (R)
… and other quantities

## Slide 29: Some Electric Components
Battery / cell: creates voltage
note: battery voltage is also called EMF (electromotive force)
Positive Terminal
Negative Terminal
Resistor:
creates resistance
(e.g. bulbs, motors, engines, …)
Wire:
conducts current
- usually made of metal
- assumed to have zero resistance
Switch: breaks or completes circuit
Open switch
Closed switch

## Slide 30: Circuit Examples
Battery voltage
Single resistor of resistance R
Current I travels from +ve to –ve terminal (slide 5), flowing through R on the way
Circuit with multiple resistors and a switch:
Current flows through both R1 and R2
Closed switch
Current flows entirely through R2 (zero current flows through R1)
Open switch
Circuit with single resistor:

## Slide 31: Circuit Examples
The circuits in the boxes below are equivalent
(because the same currents travel through the same components located on the same segments)

## Slide 32: Comparing Circuit Diagrams
Which of these is a different circuit from the others?
a.
b.
c.
d.
e.

## Slide 33: Resistors in Series and Parallel
Resistors in series: current passes sequentially through the resistors (does not branch out)
Resistors in parallel: current branches out
Resistors in series and parallel:
R1 and R2 are in series with each other
R1 and R2 are in parallel with R3

## Slide 34: Potential in a Circuit: Potential Across a Battery (measured with a voltmeter)
Battery creates a potential difference between its +ve and –ve terminals
i.e. V+ve – V-ve =
The potential at –ve terminal is assumed to be 0 V
therefore: V+ve =
e.g. a battery of 1.5 V has potential of 0 V at the –ve terminal
and 1.5 V at +ve terminal, so that potential difference is 1.5 V

## Slide 35: Potential in a Circuit: Potential Across a Resistor
As current flows through a resistor, potential dissipates/drops across the resistor [slide 14], because electrons lose energy upon collision
(connected directly to +ve terminal)
(halfway across resistor)
(connected directly to -ve terminal)
Note: potential does not change across wires because resistance of wires is zero [slide 25]

## Slide 36: V, I, R Calculations in Circuits
Kirchhoff’s Current Law (Junction Law) [slide 10]
Ohm’s Law [slide 20]: V = I R
Kirchhoff’s Voltage Law (Loop Rule)
In a closed circuit (i.e. loop), the sum of voltage drops across all components add up to the battery voltage
voltage drops across R1 and R2
Kirchhoff’s Loop Rule:

## Slide 37: V, I, R: Resistors in Series
and :
Kirchhoff’s Junction Law:
(everywhere in the circuit)
Therefore:
(because flows into R2 and flows out)
and :
Ohm’s Law: ,
Kirchhoff’s Loop Rule:
and :
Ohm’s Law (for the circuit):
(Req is the circuit’s equivalent resistance)
Kirchhoff’s Loop Rule:
Summary:
Current is the same through all resistors in series
Resistance equivalent is the sum of individual resistances
Higher resistance => Higher voltage drop across resistor

## Slide 38: V, I, R: Resistors in Parallel [1]
– 0 =
– 0 =
Potential across resistors in parallel:
– 0 =
Potential across resistors in parallel remains constant regardless of the number of resistors connected
If there are N resistors connected in parallel, every resistor will have the same voltage drop:

## Slide 39: V, I, R: Resistors in Parallel [2]
Kirchhoff’s Junction Law :
[slide 38] :
Ohm’s Law:
,
Summary:
Voltage is the same across all resistors in parallel
sum of individual ’s
Higher resistance => Lower current through resistor

## Slide 40: In General for N Resistors
Series
Adding more resistors increases Req
Parallel
Adding more resistors decreases Req
Equivalent Resistance (Req): a single resistor that has the same resistance as a group of resistors

## Slide 41: Conceptual Problem
Rank the potential at each of the points assuming that the wires are ideal (note: resistors are in both series and parallel).
VA = VC
VB = VF
VD = VE
VA = VC > VD = VE > VB = VF
+
–
A
B
C
D
E
F

## Slide 42: Example: Loop Rule
What is the current in this circuit and which way does it point (clockwise or counterclockwise)?
Start at bottom right and count up potential changes (going CCW)
= 0
= 0
= 0
(-ve CW)
Assume current is either CW or CCW (in this example, we assumed CCW)
I
3 V
1.5 V
2 W
3 W
Apply the loop rule (sum of V = 0):
Note: if the answer were positive, current would have been CCW (i.e. same as assumed direction)

## Slide 43: Example: Group of Resistors [1]
What is the equivalent resistance (Req) of this group of resistors?
10 W
10 W
20 W
30 W
10 W
Step 1: Find Req of the 10 W resistors in series
Req1 = (10 + 10) W = 20 W
Req_1= 20 W
20 W
30 W
10 W
Redraw circuit
Step 2: Find Req of the 20 W resistors in parallel
=
=> Req2 = 10 W

## Slide 44: Example: Group of Resistors [2]
Step 3: Find Req of the remaining resistors, now all in series
Req = (10 + 10 +30) W
= 50 W
Redraw circuit
30 W
10 W
Req2= 10 W

## Slide 45: Example 2: Group of Resistors [1]
What is the potential difference across the circled resistor?
2.0 V
4.0 V
6.7 V
12 V
20 V
Same set of resistors as previous
Req = 50 Ω
20 V
30 W
10 W
10 W
10 W
20 W

## Slide 46
Req = 50 W
20 V
Use Ohm’s Law for the above circuit: A = 0.4 A
Draw simplified circuit (using Req of the circuit):
Find current through the Req:
I
Example 2: Group of Resistors [2]

## Slide 47: Example 2: Group of Resistors [3]
20 V
30 W
10 W
I= 0.4 A
Req_2 = 10 W
[slide 44]
For the parallel resistors in the box, each part has same DVR
[slide 38]
i.e. VReq2 = V20Ω
10 W
10 W
20 W
Draw full circuit:

## Slide 48: Example 2: Group of Resistors [4]
What is the potential difference across the circled resistor?
2.0 V
4.0 V
6.7 V
12 V
20 V
20 V
30 W
10 W
I= 0.4 A
Req2=10 W
Find VReq2 (Ohm’s Law):
VReq2 = I Req2 = 4.0 V
V20Ω = VReq2 = 4.0 V
Note: using Ohm’s law on the 20 W resistor, the current through it can be calculated
Redraw using Req2

## Slide 49: Tips for Analyzing Combination of Resistors
Identify any groups in series
  Find equivalent resistance for each group
  Redraw circuit with Req in place of the group
Identify any groups that are in parallel
  Find equivalent resistance for each group
  Redraw circuit with Req in place of the group
Repeat until all resistors combined as much as necessary and/or possible
If looking for current or potential drop across a resistor
  Use Ohm’s Law at each
  Remember: series means same current, parallel means same potential drop across each element
  Equivalent resistor must have same total current and total potential difference

## Slide 50: Measuring Voltage
Voltmeters measure potential difference
Probes go on either side of element being measured
Therefore: voltmeter is connected in parallel
Thing Being Measured
Symbol:
V in a circle
V
That means, voltage across voltmeter is the same as the voltage across element

## Slide 51: Measuring Current
Ammeters measure charges flowing through them
Therefore: ammeter is connected in series
They get inserted into branch where current is being measured
Branch Being Measured
Symbol:
A in a circle
A
Rest of Circuit
That means, current through ammeter is the same as the current through element