## Slide 1: Cameras
OpenStax Chapter 25.6
Lens Cameras: focus image on film/CCD
Youtube: https://youtu.be/pUVdFQJTclM

## Slide 2: Pinhole Camera
A pinhole camera is a box (of paper, cardstock or something else) with a very small hole in it
Works by only allowing some light rays through
These light rays can be projected on a screen:
For a more focused picture, make hole smaller:
But now less light gets through so the picture is fainter

## Slide 3: Lens Camera
Uses a lens to form an image
Using the lens, light from object is focused on film or CCD (charge-coupled device) to create an image on it
What type of lens should it be?
We want a real image
So (if it’s a single lens) it must be a converging lens

## Slide 4: Focusing a Camera
F
F
For a given object, you want the film/CCD to be at the image location
All rays from a specific part of the object come together at the same point on the detector
blurry image if film is here
or here
Focus image by:
A – Moving lens
B – Moving film
C – Changing lens
For a given object, you want the film/CCD to be at the image location

## Slide 5: Using Thin Lens Equation to Analyze a Camera
A camera lens has a focal length of 7.0 mm; the lens is 7.2 mm from the detector when an object produces a clear image. How far is the object from the lens?
Since cameras use converging lenses to form real images, both the focal length and image distance are positive:
s' = +7.2 mm
f = +7.0 mm
=> s = 250 mm = 25 cm = 0.25 m

## Slide 6: Using Thin Lens Equation to Analyze a Camera
If the object from the previous slide fills the 9.6 mm tall sensor, how tall is the object itself?
s' = +7.2 mm
f = +7.0 mm
s = 250 mm = 25 cm = 0.25 m
We’ll need to use magnification:
Since the image is inverted we’ll use h' = – 9.6 mm

## Slide 7: Exposure Settings (time)
For a picture to turn out correctly enough light (but not too much) has to hit the detector
One way to do that is to let light hit detector for a long time
One benefit to this is easy to do
Also amount of light hitting detector is directly proportional to the time (twice the time means twice the light)
What’s a downside to having light hit the detector for more time?
Image blur

## Slide 8: Exposure Settings (Iris)
If you have a certain time for the camera to be active another way to adjust the exposure is by changing the opening through which light enters
An iris can be used to cover parts of the lens to let more or less light in
Amount of light let in is proportional to the area
© 2010 Pearson Education, Inc.

## Slide 9: Exposure Settings (Focal Length)
Which one of these would form a brighter image?
For a given lens size, focal length will make a difference in the amount of light focused on the detector
F
F
F
F
Smaller image will be brighter (light concentrated in smaller area)
Focal Length and opening size are combined in “f-number” of a camera

## Slide 10: Human Eye
OpenStax Chapter 26.1-26.2
Eyesight
  Near point: closest point eyes focus on (ciliary muscles fully contracted)
  Far point: farthest point eyes focus on (ciliary muscles fully relaxed)
Corrective Optics
  Put object at the corrected ____point (near/far point of normal adult)
  Corrective lens puts virtual image at natural _____point (near/far point of patient)
  Myopia / Nearsightedness
    Far point needs correction (it’s too near / small)
    Corrected far point should approach ∞ (very far away)
    Use diverging lens
  Hyperopia / Farsightedness
    Near point needs correction (it’s too far / big)
    Corrected near point can vary, should be about 25 cm
    Use converging lens

## Slide 11: Human Eye
Copyright © 2007, Pearson Education, Inc., publishing as Pearson Addison-Wesley.
Works by generating a real image on the retina
Works by generating a real image on the retina
Incoming rays are refracted by different parts of the eye
Indices of Refraction for Different Parts:
Aqueous humor
1.33
Lens
1.42
Vitreous humor
1.33
From: Intermediate Physics for Medicine and Biology 3rd Edition By R. K. Hobbie (© 1997 Springer-Verlag)
(eye acts like a converging lens)
(eye acts like a converging lens)

## Slide 12: Focusing the Eye
Change lens’ focal length
Reptiles, Birds, Mammals:
Copyright © 2007, Pearson Education, Inc., publishing as Pearson Addison-Wesley.
Accommodation: ciliary muscles contract / relax
Change lens’ focal length…
…by changing lens’ shape
To focus, place image at retina (detector)

## Slide 13: Changing Lens’ Shape For object getting closer and staying in focus
Thin lens equation
constant (s' = distance from lens to retina)
Increasing
(dividing by smaller number)
Has to increase
as well
This means f gets smaller
Lens shape becomes thinner or thicker?
vs.
Zoom in to first surface:
Ciliary muscles contract to reduce focal length
(“harder” to focus on near than far)

## Slide 14: Range of Vision 1
Limit to how much ciliary muscles can change the lens’s shape
s for this situation is called the Near Point
For s to be as short as possible and image still be on retina need:
About 25 cm for “normal” adults
(cannot focus on objects nearer to eye)
Lens
(Not to scale)
Lens as thick as possible
f as short as possible
Ciliary muscles fully contract

## Slide 15: Range of Vision 2
Limit to how much ciliary muscles can change the lens’s shape
s for this situation is called the Far Point
Use ∞ for “normal” adults
(cannot focus on objects farther from eye)
Lens
For s to be as long as possible and image still be on retina need:
Lens as thin as possible
f as long as possible
Ciliary muscles fully relax

## Slide 16: Near Point and Far Point
There’s a limit to how much the ciliary muscles can change the lens’ shape
Near Point
Muscles fully contracted
About 25 cm for “normal” adults
Cannot focus on objects closer to eye
Far Point
Muscles fully relaxed
Approaches ∞ for “normal” adults
Cannot focus on objects farther from eye

## Slide 17: Object Between Near and Far Point
Use Corrective Lenses if near point is too long or far point is too short
Use Corrective Lenses if near point is too long or far point is too short
Ciliary muscles contract however much they need to form focused image (of desired object) on retina
When eye focuses on something, f is set until focus changes
Lens
f as depends on how contracted the muscles need to be (for image to be on retina)
Near Point
Far Point
Can focus on anything in this range
Corrective Lenses put a (C – real; D – virtual) image between eye’s natural near and far points
Focus on this object

## Slide 18: Myopic (Near Sighted) At Far Point
Can see things that are near, but not things that are far away
To figure out how to fix, consider a point source:
At Far Point:
Myopic Eye
Eye can focus these rays onto retina
Myopic eye is fine when angle between rays is large
Closer in, the angle between the rays would be larger

## Slide 19: Myopic (Near Sighted) Farther than Far Point
Can see things that are near, but not things that are far away
To figure out how to fix, consider a point source:
Farther than Far Point:
Rays are more parallel (angle between them is smaller)
Myopic Eye brings them together before reaching retina
Myopic Eye
Myopic eye is too long
To fix, use diverging lens to spread rays out

## Slide 20: Corrective Lens (c.l.) for Myopia
Put object at corrected far point (∞)
Have c. lens put image at natural far point
Image formed by c.l. is the object for the person’s eye
Use thin lens equation to find f of c.l.
Consider if nat. f.p. < 100 m
Strongly consider if nat. f.p. < 10 m
Definitely use if nat. f.p. < 4 m
d
c = c.l.’s focal point
e = eye’s focal point
c
c
e
e
n.f.p.
corrected f.p.
|s'|
s
Consider if nat. f.p. < 100 m
Strongly consider if nat. f.p. < 10 m
Definitely use if nat. f.p. < 4 m
Have c.l. put image at natural far point (n.f.p.)
Put object at corrected far point (∞)
Consider if nat. f.p. < 100 m
Strongly consider if nat. f.p. < 10 m
Definitely use if nat. f.p. < 4 m
Consider if nat. f.p. < 100 m
Strongly consider if nat. f.p. < 10 m
Definitely use if nat. f.p. < 4 m
Notes: Powers for listed u.f.p.: Consider -0.01 D; Strongly consider -0.1 D; Definitely use -0.25 D

## Slide 21: Hyperopia (Far Sighted) At Near Point
Can see things that are far away, but not things that are close
To figure out how to fix, consider a point source:
At Near Point of Hyperopic Eye:
Hyperopic Eye
Eye can focus these rays onto retina
Hyperopic eye is fine when angle between rays is small
Further out the angle between the rays would be smaller

## Slide 22: Hyperopia (Far Sighted) Closer than Near Point
Can see things that are far away, but not things that are close
To figure out how to fix, consider a point source:
Closer than Near Point
Hyperopic Eye
Rays have a larger angle between them
Hyperopic eye brings them together behind retina
Hyperopic eye is too short
To fix, use a converging lens to bring rays closer together

## Slide 23: Corrective Lens (c.l.) for Hyperopia
Put object at corrected near point (25 cm or whatever desired)
Have c. lens put image at natural near point
Image formed by c.l. is the object for the person’s eye
Use thin lens equation to find f of c.l.
Consider if nat. n.p. > 30 cm
Strongly consider if nat. n.p. > 40 cm
Definitely use if nat. n.p. > 50 cm
d
c = c.l.’s focal point
e = eye’s focal point
c
c
e
e
corrected n.p.
eye n.p.
s
|s'|
Consider if nat. n.p. > 30 cm
Strongly consider if nat. n.p. > 40 cm
Definitely use if nat. n.p. > 50 cm
Have c. lens put image at natural near point
Put object at corrected near point (25 cm or whatever desired)
Consider if nat. n.p. > 30 cm
Strongly consider if nat. n.p. > 40 cm
Definitely use if nat. n.p. > 50 cm
Consider if nat. n.p. > 30 cm
Strongly consider if nat. n.p. > 40 cm
Definitely use if nat. n.p. > 50 cm
Notes: Powers for listed u.n.p.: Consider +0.67 D; Strongly consider +1.5 D; Definitely use +2 D

## Slide 24: Power for Corrective Lenses
Hyperopic patients require lenses with positive power
Refractive Power of a Lens is defined as:
With focal length in meters, power is measured in diopters (D)
(prescriptions do not include the D)
Sign is carried along
Myopic patients require lenses with negative power
Myopic patients require lenses with negative power
Hyperopic patients require lenses with positive power

## Slide 25: Basic Steps for Corrective Lenses
Make a sketch
Should C.L. be on the eye or some distance?
Which should be closer to the eye?
the object
the C.L.’s image
Object: where we want patient to be able to see (corrected)
Image: where patient’s eye wouldn’t need C.L. (natural)
Solve with Thin Lens Equation
Image: where patient’s eye wouldn’t need C.L. (natural)
Object: where we want patient to be able to see (corrected)

## Slide 26: Sample Question 1
A patient has a far point of 150 m; the same patient’s near point is 75 cm. Which of the following prescriptions in diopters will correct this person’s vision with contact lenses (no distance between eye and lens)?
+2.0 D
–2.0 D
+2.67 D
–2.67 D
No correction needed
Patient is hyperopic: needs a converging lens
(near point is too far; far point is not too close)
To put an image at natural near point:
s' = –0.75m (-ve because image is virtual)
Want object at corrected near point:
s = 0.25 m

## Slide 27: Sample Question 2
A patient has a far point of 70 cm; the same patient’s near point is 20 cm. Which of the following prescriptions in diopters will correct this person’s vision with contact lenses (no distance between eye and lens)?
–3.6 D
+3.6 D
+1.4 D
–1.4 D
No correction needed
Patient is myopic: needs a diverging lens
(far point is too close; near point is not too far)
To put an image at natural far point:
s' = –0.7m
Want object at corrected far point:
s → ∞

## Slide 28: Sample Question 3
To put an image at natural near point:
n = 0.40 m
s' = –(n – d)
s = c – d
A patient has a far point of 3 m; the same patient’s near point is 40 cm. To correct his vision, bifocals will be prescribed. If the bifocals will be 1.5 cm from his eye, what power in diopters will be used to correct his near vision?
–0.3 D
+1.5 D
+1.7 D
+6.5 D
+6.7 D
Fixing the hyperopia: need a converging lens
Want object at corrected near point:
c = 0.25 m
Eye
d = 1.5 cm
n
s
s = c – d = 0.235 m
s' = –(n – d) = –0.385 m
|s'|
object
image
c

## Slide 29: Sample Question 4
Want object at corrected far point:
c →∞
s' = –(u – d)
A patient has a far point of 3 m; the same patient’s near point is 40 cm. To correct his vision, bifocals will be prescribed. If the bifocals will be 1.5 cm from his eye, what power in diopters will be used to correct his distance vision?
–0.3 D
+0.3 D
–2.5 D
+2.5 D
+1.7 D
Fixing the myopia: need a diverging lens
|s'|
s' = –(u – d) = –2.985 m
image
To put an image at natural far point:
n = 3 m
n
Eye
d = 1.5 cm
s = c – d → ∞
s' = –(n – d) = –2.985 m  –3 m

## Slide 30: Human Eye in Water
(Keep in mind: myopia – image forms in front of retina; hyperopia – image forms behind retina)
The eye only works because of refraction when light goes from air to the material in the eye (where n ~ 1.4); for a human eye in water, will the eye be myopic, hyperopic or neither?
myopic
hyperopic
Myopic for far objects, hyperopic for close
Myopic for close objects, hyperopic for far
Neither
Since the index of refraction of water is n = 1.33, there will be much less refraction
Eye
In air
In water (less refraction)
What about a fish in air?

## Slide 31: Determining Conditions From Glasses
“Professor Trelawney moved into the firelight, and they saw that she was very thin; her large glasses magnified her eyes to several times their natural size, and she was draped in gauzy, spangled shawl.”
-Harry Potter and the Prisoner of Azkaban
Consider the following individual:
Prof. Trelawney’s glasses create an enlarged image
they must be converging lenses
she must have hyperopia

## Slide 32
Magnifying Glass
  Deals with angular size
  Mx is ratio of normal person’s near point (25 cm) to glass’ focal point
Angular Size
  Measure from one side of object to other
  Use right triangle to find
Magnifiers
  Use converging lens
  Put object just inside focal point

## Slide 33: Basic Magnifiers
Use a single lens to create a large upright image of the object
What type of lens could be used for that?
Diverging
Converging
With object at inside the focal point, image will be upright and magnified

## Slide 34: Apparent Size
The more space an image takes on the eye’s retina, the larger the brain interprets the corresponding object to be
Context clues are used to determine whether an object is actually smaller or just farther away
From top of a stadium, people on the field look small (apparent size is little), but you know they are not
Magnifiers increase apparent size, but how to measure it?
Removing context clues can remove ability to determine size
http://en.wikipedia.org/wiki/File:Fairway-Rock-mil-atop.jpg

## Slide 35: Apparent Size and Images
F
Consider this object and find its image
The image is larger than the object, but it is also located farther away
How can we be sure that the apparent size of the image will have increased to an observer, compared to the size of the object?
F
Apparent Size is related to Angular Size

## Slide 36: Angular Size
Angle between one side of an object/image to the other
Hold your pencil fairly close to your eye
Eye
Angular Size is q
q
Now move the pencil further away
Eye
j
Angular Size is now j

## Slide 37: Angular Size and Astronomy Eclipses vs. Transits
http://en.wikipedia.org/wiki/File:Ecl-ann.jpg
http://en.wikipedia.org/wiki/File:Mercury_transit_2.jpg
Moon and sun have similar angular sizes (when viewed from Earth)
Solar Eclipse (moon in front of sun)
Transit of Mercury (Mercury in front of sun)
Mercury and sun do not
Mercury
~1.4 times the size of the moon

## Slide 38: Angular Size and Magnifier
Angular Size of Image
(with lens)
Put object at about the focal point and compare angular size of image to the angular size of the object at a person’s near point
h
Angular Size of Object
(without lens)
length to near point ~25 cm
q0
Angular Magnification:
(for object placed at about the focal point)

## Slide 39: Microscope (OpenStax 26.4)
To get a larger magnification instead of one lens, microscopes use at least two
Objective
Creates Real image magnified by
Eye
L
Fo
Fo
Fe
Eyepiece (acts like a Magnifier)
Fe
Creates Virtual image with Angular magnification of
Overall magnification is product of objective and eyepiece’s

## Slide 40: Microscope Limit
All microscopes have a limit to how much magnification they can provide
Comes from the fact that light is not a ray
Depends on wavelength of light
We’ll discuss wave properties of light next time