## Slide 1: Circuits (contd.)
OpenStax Chapter 21.1
Youtube: https://youtu.be/FhfI4B6UmiM

## Slide 2: Resistors in Series [lecture 16-17 slide 37]
I is the same through both R1 and R2
Higher R => Higher V drop across resistor
What happens if R1 is increased (while R2 and ε are unchanged):
  increases
  I decreases
  V1 increases (and therefore, V2 decreases)
Potential at Different Locations:

## Slide 3: Resistors in Parallel [lecture 16-17 slide 39]
,
Higher R => Lower I through resistor
is always smaller than both R1 and R2
(i.e. connecting resistors in parallel reduces resistance)
Branch with larger R has smaller I
(If R1 > R2 : I1 < I2 , and vice-verse)
If R1 increases (while R2 and ε remain unchanged):
- increases
  - decreases, decreases, remains unchanged

## Slide 4: Resistors in Parallel (contd.)
When switch is opened:
- R1 is disconnected (i.e. )
- increases ()
- becomes zero (therefore: )
-
- remains unchanged
Closed switch
Open switch

## Slide 5: Resistors in Parallel and Series
ε
R2
R1
R4
R5
R3
If R3 is removed:
of R3,R4,R5 increases
(= R4 + R5)
of entire circuit increases
(= R1 + R2 + R4 + R5)
decreases
(
and decrease
increases
increases

## Slide 6: Conceptual Analysis for Current
Rank the currents through these four identical resistors:
A
B
C
D
A = B = C = D
A > B > C = D
C > B > D > A
A > B > C > D
A > C = D > B
C & D in series (i.e. same current)
From junction rule: Ileft + Iright = Itotal
Ileft
Iright
Itotal
Right & Left Branches are in parallel (have same DVbranch), but different Req
IB > ID , IC
&
use Ohm’s Law

## Slide 7: Remove Resistor in Parallel
What happens to a circuit if you remove a resistor that was in parallel with other elements?
Current still passes through the other branches
No
Do the currents on the other branches change?
Decreases
Does the total current change?

## Slide 8: Wire in Parallel with Resistor
What is the potential difference across it?
What is the current through the circled resistor?
(note: wire has zero resistance)
(must be the same as between A and B)
A
B
For an ideal wire this is:
0 V
Ohm’s Law:
Current in circled resistor must be 0 A
(“Short Circuit”)
What happened to current in other resistor?
Increased

## Slide 9: Resistances of Voltmeters and Ammeters (lecture 16-17, slides 50,51)
Large Resistance
(so that of voltmeter and R0 is almost equal to R0)
R0
V
Voltmeter: needs to be connected in parallel with resistor
(so that it has the same V across it as does the resistor)
Should voltmeter itself have large or small resistance?
Small Resistance
(so that of ammeter and R0 is almost equal to R0)
Ammeter: needs to be connected in series with resistor
(so that it has the same I through it as does the resistor)
Should ammeter itself have large or small resistance?
R0
A

## Slide 10: Energy and Power in Circuits
OpenStax Chapter 20.4

## Slide 11: Battery’s Energy Transfer
Moves particles to higher potential energy
+
–
Electric Potential Energy and Potential are related:
DU = q DV
For a battery (with DV = e) this is:
DUbatt = q e
Energy Transfer Occurring:
Echem Uelec
What happens when a resistor is included?

## Slide 12: Resistor’s Energy Transfer
+
–
Resistor
Moves particles to a lower potential energy
DUr = q DVr
For this circuit:
|DVr| = |e|
Total Energy Transfer
Echem Uelec
Battery
Echem Uelec Kions Etherm
Resistor

## Slide 13: Why Wires (and Resistors) Heat Up
As electrons move through wire, they hit ions… (lecture 16-17 slide 8)
… making ions vibrate more
(i.e. ions gain kinetic energy)
Temperature is measure of kinetic energy of atomic particles making up an object
Therefore: temperature of wire increases
Side Effect: Resistance also increases
(because electrons are more likely to hit ions now)
(This is why incandescent light bulbs heat up and light)
© 2010 Pearson Education, Inc.

## Slide 14: Electric Energy and Power
In a circuit, a battery continuously does work on the charges to keep them moving.
Therefore, instead of the total amount of work done, the rate of work done (i.e. power) is of more importance.
Work done: W = q ΔV (lecture 14-15 slide 13)
q = I Δt (lecture 16-17 slide 3)
Combining: W = I Δt ΔV
Power:
[ unit: Watts (W) = J/s ]

## Slide 15: Electric Energy and Power (contd.)
The greater the power output, the hotter/brighter/faster an element performs.
The power output of a circuit element (e.g. resistor), depends on I, V, R associated with it.
Therefore: changes in I, V, R affect power outputs of circuit elements
Power:
Also:
and:

## Slide 16: Power: Single Resistor
Power generated by battery:
Power dissipated by resistor:
(i.e. power generated by battery = power dissipated by resistor, as required by the principle of conservation of energy)
Power:

## Slide 17: Power: Resistors in Series
Power dissipated by R1 =
Power dissipated by R2 =
Power generated by battery =
If R1 > R2:
(i.e. for resistors in series, larger R dissipates more P)
I is the same through both R1 and R2
Higher R => Higher V drop across resistor
Power:

## Slide 18: Power: Resistors in Parallel
,
Higher R => Lower I through resistor
Power dissipated by R1 = =
Power dissipated by R2 = =
Power generated by battery = =
If R1 > R2:
(i.e. for resistors in parallel, larger R dissipates less P)
Power:

## Slide 19: Power: Resistors in Parallel (contd.)
Closed switch
Open switch
When switch is opened:
- R1 is disconnected (i.e. ) =>
- increases () => decreases
- becomes zero (therefore: )
-
- remains unchanged => unchanged

## Slide 20: Power: R in Parallel and Series [1]
ε
R2
R1
R4
R5
R3
If R3 is removed:
of R3,R4,R5 increases
(= R4 + R5)
of entire circuit increases
(= R1 + R2 + R4 + R5)
decreases
(
and decrease
increases
increases

## Slide 21: Power: R in Parallel and Series [2]
If R3 is removed:
of R3,R4,R5 increases
(= R4 + R5)
of entire circuit increases
(= R1 + R2 + R4 + R5)
decreases
(
and decrease
increases
increases
decreases
and decrease
increases

## Slide 22: Power Rating
A 60 W rated light bulb and a 75 W rated light bulb are both designed to work when the potential difference across them is 120 V. (i.e. bulbs consume specified power when connected to a voltage source of 120 V). The resistance of the 60 W bulb’s filament is _____ the resistance of the 75 W bulb’s filament
48 W lower than
0.4 W lower than
equal to
0.4 W higher than
48 W higher than
Find Resistance of Each Bulb:
60 W bulb:
75 W bulb:
240 W
192 W
For a given type of bulb, higher power means brighter
60 W incandescent and 15 W CFL have the same brightness
http://energystar.custhelp.com/cgi-bin/energystar.cfg/php/enduser/std_adp.php?p_faqid=2563&p_created=1148315013

## Slide 23: Conceptual Analysis of Power (similar to resistors in series)
A certain battery has two (non-ideal) wires connected to it as shown below. Both wires are made of the same material, wire 1 is three times has long as wire 2 but has one third the cross-section. How do the rates at which energy is dissipated from the two wires compare?
+
–
1
2
current in 1 = current in 2
Use this version of power:
P = I2 R
P1 = I2 R1
P2 = I2 R2
P2 = I2 (R1 / 9)
a. P1 = P2 / 3
b. P1 = 3 P2
c. P1 = P2 / 9
d. P1 = P2
e. P1 = 9 P2
= P1 / 9

## Slide 24: Conceptual Analysis with Power
Which of the following resistors will increase its thermal energy at the highest rate?
R I
2 R I
R I / 2
R / 2 I
R 2 I
Resistance
Current
Use

## Slide 25: Which is Brighter in Series?
These two bulbs are connected in series, the one with the higher resistance will be …..
Brighter
or Dimmer
In series, current is the same, and
Brighter bulb (higher power) must have higher resistance

## Slide 26: Which is Brighter in Parallel?
These two bulbs are connected in parallel, the one with the higher resistance will be …..
Brighter or
Dimmer
In parallel, potential difference is the same, and
Brighter bulb (higher power) must have lower resistance

## Slide 27: Comparing Four Identical Bulbs
One set of these bulbs is in series with power supply
One set of these bulbs is in parallel with power supply
Which is which?
Set of brighter bulbs:
Parallel
Analysis 1:
DV1 Parallel = e
DV1 Series = e / 2
Analysis 2:
I1 Series = I1 Parallel /2

## Slide 28: Removing Circuit Elements
If a single bulb is removed, what happens to the other?
Bulbs are connected in series
Bulbs are connected in parallel
goes out
Remaining bulb:
stays on

## Slide 29: Conceptual Analysis for Power
Rank the power dissipated by these four resistors. A, B, & C are identical; D has twice the resistance of the others.
A
B
C
D
A = B = C = D
A > B > C = D
D > B > C > A
A > B > D > C
A > D > B > C
IB
Iright
IA
ID = IC
RD > RC
P = I2 R
PD > PC
IA = IB + Iright
RA = RB
P = I2 R
PA > PB
DVB = DVright
IB R = Iright 3R
Iright = IB / 3
P = I2 R
PD